## Slide 1
SMART
WATERING
SYSTEM
IOT102C - GROUP2

## Slide 2
IIOT102C - GROUP2
GROUP 2 MEMBER

## Slide 3
INTRODUCTION
The Smart Watering System automates the process of dispensing water with precision, utilizing components like Arduino, sensors, and a mobile app. It allows users to select the desired amount of water, monitors consumption, and displays progress, enhancing convenience and efficiency in water management.
This project not only enhances user convenience but also promotes efficient water management, making it suitable for various applications, from household use to agricultural settings.
IIOT102C - GROUP2
Notes: Duy

## Slide 4
I2C
User Device
Watering Zone
Water pump
Water source
Arduino Uno
Physical Control Panel
Relay
Water sensor

## Slide 5
IIOT102C - GROUP2
II. METHOD & MATERIALS

## Slide 6
IOT102C - GROUP2
II. METHOD & MATERIALS
A. System Model and Block Diagram

## Slide 7
3 buttons
Module
Bluetooth
Water
Flow Sensor
Relay
Water
Pump
LCD
Screen
Arduino
UNO
Components
II. METHOD & MATERIALS
IOT102C - GROUP2
Notes: thêm ảnh
-công thức water sensor

## Slide 8
Arduino Uno
  Description: Microcontroller board with 14 I/O pins.
  Function: Acts as the central controller.
  Usage: Connects to a computer via USB.
Module Bluetooth
  Description: Wireless communication.
  Function: Receives commands from a mobile application.
  Usage: Connects to the Arduino RX and TX pins.
Water Flow Sensor
YF S401
  Description: Measures water flow rate.
  Function: Provides flow rate data.
  Usage: Connects to the input pin of the Arduino.
IOT102C - GROUP2
B. Components and Peripheral Devices
II. METHOD & MATERIALS

## Slide 9
Relay
  Description: Electrical control device.
  Function: Controls the water pump.
  Usage: Connects to the output pins of the Arduino
Water Pump
  Description: Supplies water.
  Function: Provides an accurate water flow.
  Usage: Connects to a relay.
LCD Screen (I2C)
  Description: Displays information.
  Function: Shows flow rate and status.
  Usage: Connects to the Arduino via I2C.
Buttons
  Description: Allows user interaction.
  Function: Selects the desired water volume.
  Usage: Connects to the input pins of the Arduino.
IOT102C - GROUP2
II. METHOD & MATERIALS
COMPONENTS

## Slide 10
IOT102C - GROUP2
II. METHOD & MATERIALS
Circuit DIAGRAM

## Slide 11
Water Flow Measurement System
IOT102C - GROUP2
Hall-Effect Flow Meter
  Uses a hall-effect sensor to detect water flow.
  Generates electrical pulses proportional to water volume.
  Cost-effective, but requires calibration for higher accuracy.
Key Challenge: Accuracy is affected by sensor orientation, fluid pressure, and flow variations.
Notes: thêm ảnh
-công thức water sensor

## Slide 12
Working Principle
III. PARAMETER SETUP
IOT102C - GROUP2
Pulse Generation
  Water flow rotates an impeller or turbine inside the sensor.
  A Hall-effect sensor detects each rotation and generates square wave pulses.
  Each pulse corresponds to 2.25 mL of water.
Flow Rate Calculation
  Formula: Q (L/min) = F (Hz) / 7.5
  Example: 75 Hz → 10 L/min
Notes: thêm ảnh
-công thức water sensor

## Slide 13
Working Principle
III. PARAMETER SETUP
IOT102C - GROUP2
Water Velocity & Pipe Cross-Sectional Area
  The flow rate (Q) can also be derived from water velocity (V) and pipe area (A):
  Q(m3/s)=A(m2)×V(m/s)Q (m^3/s) = A (m^2) × V (m/s)Q(m3/s)=A(m2)×V(m/s)
  Conversion to L/min:
  1m3/s=60,000L/min1 m^3/s = 60,000 L/min1m3/s=60,000L/min
Total Water Volume Calculation
  Total water volume passing through the sensor over time t (seconds):
  Volume(L) = Total Pulses / (7.5 × 60)
  Example: 4,500 pulses in 60 seconds → 10 L.
Notes: thêm ảnh
-công thức water sensor

## Slide 14
II. METHOD & MATERIALS
INTERFACING BETWEEN ARDUINO UNO AND ITS COMPONENTS
Notes: KHÁNH

## Slide 15
II. METHOD & MATERIALS
Bluetooth Serial Connection Implementation
Step 1: Enable Bluetooth on Mobile
→ Turn on Bluetooth in device settings (Settings → Bluetooth).
Notes: KHÁNH

## Slide 16
II. METHOD & MATERIALS
Bluetooth Serial Connection Implementation
Step 2: Pair with HC-05 Module
→ Search for "Water Pouring B05", tap to pair, and enter PIN 1234 or 0000.
Notes: KHÁNH

## Slide 17
II. METHOD & MATERIALS
Bluetooth Serial Connection Implementation
Step 3: Establish Connection
→ In a Bluetooth terminal app, select HC-05 and tap "Connect".
Notes: KHÁNH

## Slide 18
II. METHOD & MATERIALS
Bluetooth Serial Connection Implementation
Step 4: Send Data to Arduino
→ Type a number (e.g., 100) in the app and press "Send".
Notes: KHÁNH

## Slide 19
II. METHOD & MATERIALS
Bluetooth Serial Connection Implementation
Step 5: Verify Communication
→ Check the Arduino Serial Monitor (9600 baud rate) for received data. If issues occur, verify baud rate & wiring.
Notes: KHÁNH

## Slide 20
IOT102C - GROUP2
PROGRAMING FLOWCHART
II. METHOD & MATERIALS

## Slide 21
PROGRAMING FLOWCHART
II. METHOD & MATERIALS
Step 1: System Initialization & LCD Activation
  System starts, verifying connections (LCD, sensor, relay, Bluetooth).
  Displays system information for 650ms.
  LCD shows "SYSTEM READY" when initialization is complete.
Step 2: User Input Reception & Validation
  Receives input from buttons or mobile app.
  Validates water volume (100-2000mL).
  If invalid → displays error on LCD and app.
Notes: thêm ảnh
-công thức water sensor

## Slide 22
PROGRAMING FLOWCHART
II. METHOD & MATERIALS
Step 3: Pump Activation & Flow Control
  If valid → activates pump via relay.
  Hall-effect sensor counts pulses, measuring water flow.
  PID control adjusts pump speed for accuracy.
Step 4: Real-Time Progress Monitoring
  LCD and app display progress percentage.
  Updates volume every 50ms, estimates remaining time.
Notes: thêm ảnh
-công thức water sensor

## Slide 23
PROGRAMING FLOWCHART
II. METHOD & MATERIALS
Step 5: Target Volume Verification & Pump Shutdown
  At 98% target → gradually slows pump over 300ms.
  Stops pump precisely at 100%, preventing backflow.
Step 6: Final Display & Data Reporting
  LCD & app show final volume (e.g., "FINISHED 487mL").
  Saves transaction to EEPROM & sends confirmation via Bluetooth.
Step 7: Continuous Operation Cycle
  Stops pump, prevents overflow, and displays completion message.
  After 5 seconds, the system returns to standby mode, ready for the next input.
Notes: thêm ảnh
-công thức water sensor

## Slide 24
IIOT102C - GROUP2
III. RESULTS AND DISCUSSION

## Slide 25
  ±10% accuracy in volume measurement.
  Dual control: Physical buttons & Bluetooth app.
  Energy-efficient pump operation.
  Low production cost (<$50), making it ideal for small-scale beverage, lab, and agricultural applications.
DISCUSSION - ADVANTAGES

## Slide 26
  Corrosion-resistant materials for durability.
  Temperature compensation for accurate viscosity-based measurement.
  Bluetooth 5.0 for extended wireless range.
  Smart features: Usage analysis & predictive maintenance.
DISCUSSION - DISADVANTAGES

## Slide 27
CONCLUSION
III. RESULTS AND DISCUSSION
=> This project lays a strong foundation for next-gen liquid handling systems, ensuring adaptability for commercial & industrial applications, with a cost-effective & user-friendly design ready for potential commercialization.
Notes: thêm ảnh
-công thức water sensor

## Slide 28
THANK YOU
FOR YOUR ATTENTION
IOT102C - GROUP2